## 1.0 Basic Operation

See 2.1 Control Panel Layout for the names and locations of the control panel elements and descriptions.

Switch the light control system on via the power switch. The voltage indicator will illuminate and indicate the launch point battery voltage while the system is switched on.

The system draws only a very small amount of quiescent power and may be left on continuously during winch launching operations. It must be switched off at the end of the day when the launch point cabin battery is put onto charge.

Glider Launch Sequence:
1. Press and hold the up slack button to display the “take up slack” sequence on the signal lights. The system will emanate regular bleeps.
2. To display the “all out” sequence, release the up slack button, then press and hold the all out button. The system will emanate rapid bleeps.
3. Once the glider is established in the climb, release the all out button to cease further signals.

If it is necessary to stop the launch, press the stop button. The system will enter stop mode, in which it will display the stop light signal, and will emit a continuous bleep.
It is the responsibility of all persons present to stop a launch if they identify any reason why it cannot safely continue. You must immediately press the stop button if any person shouts or indicates “Stop”.

To cancel stop mode, once the apparent hazard has been established and eliminated, press and release both the up slack and all out buttons simultaneously.

## 2.0 Description

### 2.1 Control Panel Layout